## Slide 1
陳培殷老師
國立成功大學 資訊工程系
數位系統實驗

## Slide 2
陳培殷老師
國立成功大學 資訊工程系
LAB - 02

## Slide 3: Three representations for a circuit
F1=x+y’z
1. Boolean Algebra
3. Circuit Diagram
2. Truth Table
Inputs
n input variables  2n combinations
真值表

## Slide 4: Equipment
Names | Amount
Solerless Breadboard | ×1
74LS00 | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 5: Lab notice
Input
Output

## Slide 6: Lab notice
Correct
VCC：
GND：

## Slide 7: Lab notice
Wrong
Overlap

## Slide 8: Lab notice
Correct
VCC：
GND：

## Slide 9: Lab notice
Correct
VCC：
GND：

## Slide 10: Lab notice
A
B
A
B

## Slide 11: Lab notice
A
B
A

## Slide 12: Lab 02_1
Please draw their Truth Tables and implement the circuits with breadboard.
  F1(A, B) = (A + B)’(A’ + B’)
  F2(A, B) = A’+ AB
A | B | F1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | F2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Notes: 錯誤：此時不需化簡(已修正)

## Slide 13
  A half adder (HA) consists of two inputs (A and B) and two outputs (Sum and Carry). “A” denotes the summand and “B” is the addend. Sum and Carry mean the output sum and carry for input “A” and “B”. The truth table and Boolean algebra for the half adder are as follows.
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
  F(A, B) = A’B’ + A’B + AB’ + AB
Lab 02_2 - Half Adder (1/2)

## Slide 14
Please
  (a) draw the circuit diagram of the half adder according
  to the truth table shown in previous page.
  (b) implement the circuit on the breadboard.
Lab 02_2 - Half Adder (2/2)

## Slide 15
There are two inputs denoted as A and B. Both A and B are 1-bit value. A comparator is designed to determine whether A is equal to B or not. The output results are represented with E .
The function and truth table of the comparator is described as follows.
  E =
Lab 02_3 – Comparator(1/2)

## Slide 16
Please
  (a) draw the truth table of the comparator.
  (b) draw the circuit diagram of the comparator.
  (c) implement the circuit on the breadboard.
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
  F(A, B) = (A’B’) + (AB)
  F(A, B) = A’B’ + A’B + AB’ + AB
Lab 02_3 – Comparator(2/2)