## Slide 1
陳培殷老師
國立成功大學 資訊工程系
數位系統實驗

## Slide 2
陳培殷老師
國立成功大學 資訊工程系
LAB - 03

## Slide 3
There is a 2-bit input X (represented as X1 and X0). A constant multiplier is designed to multiply the input by 3. Finally, show the result with decimal format (0, 1, 2, …..,9) on Digital Display in the breadboard.
Hint-1:
The output digital number is 0, 3, 6 or 9, respectively, for four different inputs (0, 1, 2, 3).
Lab I -- Constant Multiplier (1/3)
MSB

## Slide 4
D | C | B | A | DIGITAL DISPLAY
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
Hint-2:
Function of the Digital Display in the breadboard is as follows.
Lab I -- Constant Multiplier (2/3)

## Slide 5
Please
  (a) draw the truth table of the constant multiplier where two input bits are X1 and X0, and four output bits are A, B, C and D, respectively.
  (b) simplify the circuit with K-map (SOP format) and draw the simplified circuit diagram of the constant multiplier.
  (c) implement the circuit on the breadboard.
Lab I -- Constant Multiplier (3/3)

## Slide 6
Names | Amount
Solerless Breadboard | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1
Components needed for LAB I

## Slide 7
There are a 3-bit input X (represented as X2, X1 and X0) and two 1-bit outputs A and B. The comparator is designed to let output A be 1 if X>3 and output B be 1 if X>4.
The function of the comparator is described as follows.
  A =
  B =
MSB
LSB
Lab II – Comparator(1/2)

## Slide 8
Please
  (a) draw the truth table of the comparator where three input bits are X2, X1 and X0, and two output bits are A and B, respectively.
  (b) simplify the circuit with K-map and draw the simplified SOP-format circuit diagram of the constant multiplier. Finally, implement the circuit on the breadboard.
  (c) repeat (b) by using the POS format.
Lab II – Comparator(2/2)

## Slide 9
Names | Amount
Solerless Breadboard | ×1
74LS08 | ×1
74LS32 | ×1
Components needed for LAB II

## Slide 10
74LS04

## Slide 11
74LS08
Notes: 1.上排的VCC並不是整排連在一起
2.實驗三的A、B只要接右上角的output

## Slide 12
74LS32