## Slide 1: LAB - 04
陳培殷老師
國立成功大學 資訊工程系

## Slide 2: Install Quartus II
下載網址 - https://reurl.cc/eOQK7Q

## Slide 3: Install Quartus II
解壓縮後打開setup.bat

## Slide 4: Install Quartus II
一直按Next

## Slide 5: Install Quartus II
勾選選項

## Slide 6: Install Quartus II
完成後勾選Launch USB Blaster II driver installation

## Slide 7: Install Quartus II
跳出裝置驅動程式安裝精靈後一直按下一步

## Slide 8: Install Quartus II
出現 “可以使用” 就完成安裝了

## Slide 9: Quartus II Tutorial (1/19)
Getting Started –
  Start the Quartus II software

## Slide 10
Quartus II Tutorial (2/19)
Create a New Project –
  Open New Project Wizard (File → New Project Wizard…)

## Slide 11
Specify the working directory and the name of the project
可先新增資料夾
請記住!名稱要相同
Quartus II Tutorial (3/19)

## Slide 12: Quartus II Tutorial (4/19)
Select “Empty project”. Then, click “Next”.
Select design files. Or click “Next” to skip this step.

## Slide 13: Quartus II Tutorial (5/19)
Specify device settings - (DE0-CV Device family are used). Click “Next.”
5CEFA4F23C7

## Slide 14: Quartus II Tutorial (6/19)
Specify EDA Tool – (Modelsim-Altera is selected for simulation). Click “Finish.”

## Slide 15: Quartus II Tutorial (7/19)
Edit a new file by opening a Verilog HDL file
  (File → New → Verilog HDL File → OK)

## Slide 16: Quartus II Tutorial (8/19)
Write Verilog code
Top module name 一定要跟 Project name 相同 !!
輸入(input) |  | 輸出(output) | 
被加數(a) | 加數(b) | 和(sum) | 進位(carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1: | //File Name：Half_Adder.v
2: | module half_adder(a, b, sum, carry);
3: | input a, b;
4: | output sum, carry;
5: | 
6: | assign sum = a ^ b;
7: | assign carry = a & b;
8: | 
9: | endmodule

## Slide 17: Quartus II Tutorial (9/19)
Compiling the Designed Circuit (synthesis 合成)
  (Processing → Start Compilation)

## Slide 18: Quartus II Tutorial (10/19)
Successful compilation

## Slide 19: Quartus II Tutorial (11/19)
Edit a new file by opening a Verilog HDL file
  (File → New → University Program VWF→ OK)

## Slide 20: Quartus II Simulation (12/19)
Simulating the Designed Circuit
  Use node finder to find all the I/O pins (Edit → Insert → Insert Node or Bus…)

## Slide 21: Quartus II Simulation (13/19)
Simulating the Designed Circuit
  Selecting nodes to insert into the Waveform Editor
沒跑出pin腳，表示你剛剛忘記compile
全選

## Slide 22: Quartus II Simulation (14/19)
Simulating the Designed Circuit
  Selecting nodes to insert into the Waveform Editor

## Slide 23: Quartus II Simulation (15/19)
Simulating the Designed Circuit
  Select and edit waveform
按住並拖曳即可選取

## Slide 24: Quartus II Simulation (16/19)
Simulating the Designed Circuit
  Setting of test values

## Slide 25: Quartus II Simulation (17/19)
Simulating the Designed Circuit
  Run Functional Simulation

## Slide 26: Quartus II Simulation (18/19)
Simulating the Designed Circuit
  Save .vwf

## Slide 27: Quartus II Simulation (19/19)
The result of functional simulation
輸入(input) |  | 輸出(output) | 
被加數(a) | 加數(b) | 和(sum) | 進位(carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 28: Quartus II Simulation Notice
如果simulation時出現error，修改ModelSim-Altera路徑
  (Tools → Options → EDA Tool Options → ModelSim-Altera → C:\intelFPGA_lite\18.1\modelsim_ase\win32aloem)

## Slide 29: Lab I - Half Adder
and
01
xor
01
a
b
sum
c_out

## Slide 30: Lab I - Half Adder
(a) Using Verilog to implement a 1-bit Half Adder
    Please implement with 3 methods
      Structural description
      Data flow description
      Behavioral description
(b) Simulation with waveform

## Slide 31
Lab I - Hint

## Slide 32
Lab I - Hint

## Slide 33
Lab I - Hint

## Slide 34
Lab I - Simulation with waveform
a | b | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 35
Lab II - Full Adder (1/2)

## Slide 36
Lab II - Full Adder (2/2)
c_in
a
b
sum
c_out
(a⊕b) ⊕ c_in
a sum
Add_half
b c_out
a sum
Add_half
b c_out
w3
(a⊕b) c_in
M2
M1
w1
(a⊕b)
ab
(a⊕b) c_in + ab
w2
You can implement a full adder with (2 half adder and 1 or gate).

## Slide 37
(a) Using Verilog to implement a 1-bit Full Adder
    Please implement with 3 methods
      Structural description(with 2 half adder + 1 or gate)
      Data flow description
      Behavioral description
(b) Simulation with waveform
Lab II - Full Adder

## Slide 38: Lab II - Simulation with waveform
z | y | x | S | C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 39
Notice
請勿在桌面建立 Project 及請勿命名中文資料夾
Device family 請確認與 FPGA Chip 符合 (5CEFA4F23C7)
Top module name & Project name 需要一致
確認 module … endmodule 為keyword 變成藍色字體